## Slide 1: Pipelined Processor Demo
Bruno Peynetti, Jacob Kobza

## Slide 2: Processor Overview
Top Level contains I-Memory, D-Memory and Pipeline Processor (processor must be separate for synthesis)
Pipeline Processor components fall under the following categories:
  Pipeline Registers
  Pipeline Stages
  Register File and PC
  Hazard Detection
Pipeline Processor module contains mostly wiring between stages, hazard detection and registers

## Slide 3: The Big Picture: Overall Pipeline Datapath

## Slide 4: Pipeline Registers
Pipeline registers are arrays of flip flops that pass all necessary data between pipeline stages
Registers vary in size depending on what data is needed in the next stage
Input to registers includes a “flush” bit, which sets all values in the register to zero if a stall or jump/branch occurs

## Slide 5: Example: ID/EX and MEM/WB Registers

## Slide 6: Pipeline Stages
Each pipeline stage takes the output from the register before it (not applicable for IF) and outputs the values needed for the next register (not applicable for WB)
In order to interact with I-Memory or D-Memory, stages must pass all the inputs for the memory unit up to the top level

## Slide 7: Pipeline Stage/Register Interface

## Slide 8: Register File
Needs to be accessed in ID and WB stages, so placed in the top level of the pipeline processor
Same design as single cycle processor

## Slide 9: PC and PC Logic
PC implemented in IF stage, where PC is used to fetch next instruction from I-memory
“PC Logic” component from single cycle processor spread between IF and EX stages
“check_branch” component from single cycle still used to check if branch or jump occurs
Leap_out and leap_addr taken from the output of the EX/MEM pipeline register

## Slide 10: Hazard Detection
We looked at each possible hazard and solved each one with one module
Then consolidated hazard detection into fewer modules (after a lot of debugging)
  MEM_EX_HAZARD
  WB_EX_HAZARD
  WB_MEM_HAZARD -> later deleted
  STALL_LOAD_HAZARD
  WB_ID_HAZARD

## Slide 11: Example: WB/EX Hazard Detection

## Slide 12: Top Level Hazard Detection Interface

## Slide 13: Synthesis Results
Area : 18000 um2
Timing : (800 MHz) -> MET

## Slide 14: Issues While Building
Attempted to keep modularity
  Caused many unnecessary signals that were later removed by synthesis
PC Logic
  When stalling, we block the write enable
Jump/Branch
  Flush registers and modify nextPC
  Determine what to flush, what to stall
Trap detection
  Executed in MEM stage to avoid unwanted writes to memory and/or registers

## Slide 15: FIBONACCI DEMO: WHAT YOU’VE ALL BEEN WAITING FOR